## Slide 1: Implementation and Hardware Accelerated Verification of a Connected Component Labeling Architecture
Diploma Thesis
Examiner: Prof. Dr.-Ing. S. Simon
Supervisor: M. Sc. Yousef Baroud
Notes: Hello every one, my name is… I’ll present you now my thesis with the title:

## Slide 2: Outline
Motivation
Goals
Proposed Design
  CCL Reference implementation
  Hardware Verification Architecture
Software
Results
Conclusion
Notes: This is the outline for my presentation 21…22…23 at the end you can see a demo of the implemented architecture if you are interested
-> Now we start with the motivation

## Slide 3: Motivation
Proof correctness of image processing algorithm
Testing with list of testcases – incomplete
Using exhaustive testing
  Formal verification methods - do not work in every case
  Verification by simulation - slow
Testing requires >80% of development time [FGP10]
  Support the developer
Notes: New algorithm -> check correctness
In Terms -> fulfilment of specification
Formal verification methods not work for most img algos
4x4 image exhaustive ~30min
->To support the developer with the testing we want to build a architecture to verify the correctness of a single pass CCL

## Slide 4: Goals
Verify correctness of single pass CCL
Automatic output verification for input stimuli
Using exhaustive testing – reasonable image size
Reference CCL implementation
Speedup verification with FPGA
Send found errors to PC
Non exhaustive test for bigger image size
COMPARATOR
CCL-DUT
CCL-REF
STIM-GEN
ERR
Notes: -> We heard now multiple times about CCL. I know most of you know what this is, so I just give a brief explination

## Slide 5: Connected Component Labeling
Assign unique labels to connected pixels
1
1
1
1
1
1
4
4
4
Notes: -> The most intuitive way to do the labeling for a raster scan image is a two pass ccl algorithm.

## Slide 6: Connected Component Labeling
1
1
1
3
2
2
5
4
4
1
1
1
1
1
1
4
4
4
2-pass Connected Component Labeling
Proposed Design – 2-pass CCL
3
2
3
1
5
4
1
1
2
1
3
1
4
4
5
4
first-pass
equivalence table
lookup table generation
second-pass
Bounding boxes
A
D
B
C
X
Neighborhood of pixel X
Notes: It is really intuitive
-> This algorithm is used for the reference CCL and next we will see how this is implemented

## Slide 7: Proposed Design – CCL REF
1
1
1
3
2
2
5
4
4
LABELING
EQUI
LABEL
FIFO
3
2
3
1
5
4
1
1
2
1
3
1
4
4
5
4
1
1
1
1
1
1
4
4
4
RAM
LU TABLE
PX
PX BUF
BOUNDBOX
BOX
CCL-REF
CONTROL UNIT
ERROR
Notes: Internal error: for ex. a fifo overflow or if more labels are required as expected
Don’t forget the the Finite state machine
->FSM!!! another more advanced way to do the labeling is implemented by the dut

## Slide 8: Proposed Design – CCL-DUT
Single-pass CCL M. Klaiber et al. [KRW+12]
Used as a black box
CLK
RESET
READY
PX_VALID
PX_VALUE
BOX_VALID
BOX_DATA
ERROR
Notes: Single pass, parallel, storage optimized implementation
Most of you know this approach better than I do.
Errors of failed assertions
->The last component to do the automatic exhaustive test is the comparator. It should report 4 different error types.

## Slide 9: Proposed Design – Comparator
4 different outputs
  NO ERROR
  2. + 3. Number of Boxes mismatch
  4. BOXES CCL-DUT BOXES CCL-REF
3 approaches
  CMP1 : sorting before compare
    sorting + compare =
  CMP2: compare all
  CMP3: sorting while inserting
    compare
3
8
9
1
4
4
1
9
8
3
Notes: Recognise
Now we have three different approaches
->Only the Type2 and 3 has been implemented Type 3 is not explained here. Type 2 stores the left list in a fifo, since every value needs only be looked once. The right list is stored in a RAM

## Slide 10: Proposed Design – Comparator 2
RAM
DATA_IN
IN_ADR
DATA_OUT
OUT_ADR
ADR CNT
IN_REF
ADR CNT
CONTROL-UNIT
FIFO
DATA_IN
DATA_OUT
READ
FILL LVL
IN_DUT
LAST_IN
COMPARATOR
Notes: ADR-CNT
-> Now we can put all together and the we have a automatic verifier…

## Slide 11: Proposed Design – Verifier Architecture
STIM-GEN
FIFO
COMPARATOR
CCL-DUT
CCL-REF
U
VERIFIER
COM-CONTROL
UDP-ENC
UDP-DEC
UDP/IP-Core
ETHERNET-MAC
TOP
Internal Error
Bounding Box
CMP Error
Notes: Stimgen for input
Fifo to store the output
2 behaviors if fifo is full:
dropp errors
Stall verifier
COM Control sends Fifo data -> UDP ->IP -> ETH to PC
Set start/end stimulus
~3% utilization of Virtex-6
-> We can use the free space to speedup the architecture by implementing more verifiers in parallel

## Slide 12: Verification Architecture - Speedup
Intuitive parallelization of CCL-DUT, CCL-REF and COMPARATOR
VERIFIER
ARBITER
ARBITER
COMPARATOR
CCL-DUT
CCL-REF
U
1
2
N
Notes: We choosen the most intuitive way to speed the architecture up
Replicating units
Utilization now is nearly 100% and speedup factor of ~70
->Can we further increase the performance?

## Slide 13: Verification Architecture – Speedup 2
Chart: Different labeled areas per image over exhaustive test run
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
5x5 Image Size | 0.44003 | 0.33459 | 0.16479 | 0.050899 | 0.0086738 | 0.00093734 | 6.5684e-05 | 2.414e-06 | 2.9802e-08
6x5 Image Size | 0.38993 | 0.33915 | 0.18446 | 0.067381 | 0.016287 | 0.0025273 | 0.00024779 | 1.3688e-05 | 3.1944e-07
6x6 Image Size | 0.35035 | 0.33776 | 0.19788 | 0.08303 | 0.024825 | 0.0053032 | 0.00077994 | 7.104e-05 | 2.882e-06
Images with different complexity
          5x5 Image – one input for 9 boxes
Notes: -> This can be used to implement smaller instances to process the simple images and for the complexer images we instantiate a instances which can process every input image type.

## Slide 14: Verification Architecture – Speedup 2
COMPARATOR
CCL-REF
CCL-DUT
U
VERIFIER
ARBITER
ARBITER
COMPARATOR
CCL-REF
U
RERUN
FIFO
CCL-DUT
Notes: This advanced architecture has not been implemented
-> we now know how the hardware architecture looks like. Let’s now give a look on the software….

## Slide 15: Software - Verifier
Interface to testbench of CCL-DUT/CCL-REF
VHDL image reader library (PBM)
Compares with results of software CCL implementation
Run simulation for a single image or for a list of images
VHDL-Testbench
DUT/REF
Software CCL
Box output
Software Verifier
../img/test33.pbm
../img/test34.pbm
../img/test35.pbm
../img/test36.pbm
../img/test37.pbm
../img/test38.pbm
../img/test39.pbm errors:2
../img/test40.pbm
Verification failed
Result of image test list
Single image test
Notes: Before we come to the software which communicates with the HW arch
-> Now we come to the software which interfaces the architecture on the FPGA…

## Slide 16: Software – Error Inspector
Notes: A Data Logger command line tool reads and stores the found errors as JSON
This JSON logs can be viewed with the error inspector
->Here we only can analyze error image by error image. To get a global view on the errors a visualization as a heatmap has been implemented

## Slide 17: Software – Error Heatmap
Notes: We can see here which pixels was involved in error images
-> More of the software can be seen in the demo and we go on with the result section.

## Slide 18: Results Speed
Exhaustive test run for different image sizes
Xilinx Virtex-6 LX-240 (xc6vlx240t-ff1759-2) run on 125 MHz
ModelSim simulation ~30 min for 4 x 4 image (Intel i7-3770)
6 x 6 requires longer ~60 years
Size | CMP 2 | CMP 3
4 x 4 | 38 ms* | 36ms*
6 x 6 | 18:48h* | 18:24h*
2 x 18 | 1d 03:57h* | 1d 02:50h*
21 x 2 | 69d 02:26h* | 61d 22:22h*
Size |  | 
4 x 4 | 38 ms* | 36ms*
6 x 6 | 18:48h* | 18:24h*
2 x 18 | 1d 03:57h* | 1d 02:50h*
21 x 2 | 69d 02:26h* | 61d 22:22h*
* Interpolated value
Notes: Here you can see the runtime for exhaustive testing for different image sizes
Diff CMP, CMP is as expected faster
-> This runtime could be reduced with the parallelization

## Slide 19: Results Speed – Parallel Instances
Size | CMP 2 |  | CMP 3 | 
 | instances | runtime | instances | runtime
4 x 4 | 95 | 525 µs | 95 | 581µs
6 x 6 | 86 | 00:13h | 70 | 00:16h
2 x 18 | 84 | 00:19h | 69 | 00:23h
21 x 2 | 75 | 22:06h | 58 | 1d 01:37h
9 x 5 | 75 | 6d 12:35h | 57 | -
Size |  |  |  | 
 | instances | runtime | instances | runtime
4 x 4 | 95 | 525 µs | 95 | 581µs
6 x 6 | 86 | 00:13h | 70 | 00:16h
2 x 18 | 84 | 00:19h | 69 | 00:23h
21 x 2 | 75 | 22:06h | 58 | 1d 01:37h
9 x 5 | 75 | 6d 12:35h | 57 | -
Exhaustive test run for different image sizes
Maximum number of instances
Notes: You can see the maximum number of instances which fit into the fpga
Now the CMP2 is faster…
->So we could reduce the runtime to a point where it is possible to process a 9x5 image in lesser than a week
(missing value ~8.5 days)

## Slide 20: Results Speed - Runtime
Chart: Image size in pixels
| 16 | 36 | 42 | 45 | 50 | 55 | 64
FPGA | 1.6648e-11 | 2.4734e-05 | 0.0025228 | 0.017875 | 0.57199 | 18.3038 | 9371.5482
ModelSim Simulation | 5.7078e-05 | 59.8502 | 3830.4146 | 30643.3169 | 980586.1406 | 31378756.5005 | 16065923328.2338
Exhaustive test runtime in years
Notes: 8x8
FPGA ~10,000 years
Software ~16 Billion years
Started at the big bang
It will be done in ~2 Billion years
Universe ~14 Billion years
To reduce fpga runtime to ~1day -> ~4 million FPGA required
-> Now let’s see how many errors are found in the DUT

## Slide 21: Results
>12 revisions of CCL-DUT exhaustive tested (6 x 6)
Chart: 
| 1 | 2 | 3 | 4
Total number of found errors in last 4 revisions | 840000000 | 4300000000 | 601000000 | 0
Notes: More than 12 revisions of the DUT has been tested
2 we introduced the reporting of internal errors
-> we also tested different image sizes a overview…

## Slide 22: Results
Chart: Found discrepancies for different image size in %
| 2x1 | 2x3 | 3x2 | 3x3 | 4x3 | 3x4 | 4x4 | 5x4 | 4x5 | 5x5 | 6x6 | 18x2 | 21x2 | 9x5
Found discrepancies | 0 | 0 | 0.51 | 0 | 0.165 | 0.225 | 0.796 | 0.0004 | 0.0005 | 1.3e-05 | 0 | 0.1001 | 0.1247 | 0.0002
Notes: … of the found errors can be found in this chart
Problem with sizes 2 to the power of…
-> also a image size of 63x61 has been tested…

## Slide 23: Result – Non exhaustive test
Test image generator
  Predefined pattern
  Random noise
1000 images 63 x 61
  Different pattern density
  Different noise level
No errors found
Figure 1: Predefined pattern
Figure 2: Sample image
Notes: … but not in a exhaustive way.
Test run in Software
->Now we come to the conclusion

## Slide 24: Conclusion
Implementation of CCL-REF and verifier architecture
Software for reporting and visualizing errors
Interface to ModelSim Simulation
Proof correctness of image processing algorithm for some sizes
Different image sizes exhaustive tested
6 x 6 image errors from
Bigger image size tested with random images
Notes: 800 million errors
-> before I end a short outlook what can be done on this topic

## Slide 25: Future Work Recommandation
CCL-REF instances for different complex images
Fully pipelined CCL-REF
Extend to generic verification architecture

## Slide 26: Questions/Demo
Questions?

## Slide 27
[KRW+12] M. Klaiber, L. Rockstroh, Z. Wang, Y. Baroud, S. Simon. A memory- efficient parallel single pass architecture for connected component labeling of streamed images. In Field-Programmable Technology (FPT), 2012 International Conference on, pp. 159–165. IEEE, 2012.
[FGP10] M. Fujita, I. Ghosh, M. Prasad. Verification techniques for system-level design. Morgan Kaufmann, 2010

## Slide 28: Result - Speed
lesser is better
Chart: average clocks per pixel one instance
| 4 x 4 | 2 x 18 | 6 x 6 | 21 x 2 | 9 x 5
Comparator Type 2 | 4.5 | 5.1 | 3.4 | 4.04 | 3.1
Comparator Type 3 | 4.4 | 5 | 3.2 | 3.6

## Slide 29: Result - Speed
Chart: average clocks per pixel max instances
| 4 x 4 | 2 x 18 | 6 x 6 | 21 x 2 | 9 x 5
Comparator Type 2 | 0.042 | 0.059 | 0.038 | 0.054 | 0.042
Comparator Type 3 | 0.047 | 0.072 | 0.046 | 0.062

## Slide 30: Size of CCL-REF
Entity | Max Clock | Register | Logic LUTs | Memory LUTs
LABELING | 313 MHz | 52 | 151 | 8
LU TABLE | 250 MHz | 116 | 225 | 8
BOUNDBOX | 330 MHz | 42 | 117 | 24
CCL with BOUNDBOX | 250 MHz | 233 | 569 | 42

## Slide 31: Comparison of CMP
Size | Max Box | CMP | Speed | LUTs
8x6 | 12 | Type 2 | 291 MHz | 221
 |  | Type 3 | 227 MHz | 1828
9x5 | 15 | Type 2 | 230 MHz | 301
 |  | Type 3 | 170 MHz | 2430
6x6 | 9 | Type 2 | 289 MHz | 197
 |  | Type 3 | 251 MHz | 750
4x4 | 4 | Type 2 | 343 MHz | 110
 |  | Type 3 | 355 MHz | 156

## Slide 32: Size of Verification Architecture
Size | Max Clock | Register | LUTs | BRAMs
4 x 4 | 125 MHz | 3180 | 5646 | 5
6 x 6 | 125 MHz | 3649 | 6680 | 5
21 x 2 | 125 MHz | 3827 | 7052 | 5
9 x 5 | 125 MHz | 3876 | 7339 | 5

## Slide 33: Error Heatmap Calculation
Stimulus:
In verification stimuli 1, 2, 3, 5 error occurred
+++=
3 | 
2 | 
1 | 
0 | 

## Slide 34: Proposed Design – Comparator 3
IN_REF
IN_DUT
BOX 1
BOX 2
BOX n
SHIFT-SELECTOR
BOX 1
BOX 2
BOX n
SHIFT-SELECTOR
ERR-GEN